## Slide 2
Who We Are
Foto
Foto
Christian Gilli
Software Engineer
MSc
7+ years in the pro audio industry
Performance optimisation of numerical software
Michele Mirabella
Electronic Engineer
PhD Student in ICT
High mobility comm. towards 6G
Joint communication and sensing (JCAS) systems

## Slide 3
Outline
What is sample rate conversion and why it is important
Mathematical foundations of sample rate conversion
What makes a good sample rate converter
Comparison of different implementations

## Slide 4
Intro: Sample Rate Conversion
Sample Rate Conversion (SRC) is the process of converting discrete samples from one sample rate to a different sample rate.
Sampling: measuring the signal amplitude at even intervals
Sample: a single measurement of a waveform/signal
Sample Rate: the frequency at which samples are taken per second (Hz)

## Slide 5
Why Sample Sate Conversion?
Typically, digital audio is recorded, stored and played back at more than one sample rate
In both the audio recording and playback, it is often necessary or convenient to synchronize streams at different frequencies.
Distribution media limited support (e.g., CDs only support 44.1 kHz sample rates)
No standard sample rate for audio recording
Mixed audio-video systems operating at different frequencies [1]
[1]: https://www.directout.eu/
Notes: Decidiamo se mettere questi dettagli in un’altra slide. Sample rate Usage44.1 kHz:Audio cd quality and the most commonly used sample rate in music recordings.48 kHz:Professional digital video equipment and also the sampling rate of a lot of professional audio gear such as mixers and recorders.88.2 kHz:Not often used – doubling of the cd-quality, can sometimes be found.96 kHz:DVD audio quality from stereo-mixes up 5.1-surround-mixes.192 kHz:DVD audio quality for stereo-mixes.

## Slide 6
SRC Theory
Notes: Aliases out of audible range may still be a problem, not for our ears but for audio devices (e.g., your tweeters might not like them) and processors.

## Slide 7
SRC Theory
Core operations:
Upsample:
Downsample:
L↑
M↓
Notes: Aliases out of audible range may still be a problem, not for our ears but for audio devices (e.g., your tweeters might not like them) and processors.

## Slide 8
SRC Theory
Core operations:
Upsample:
Downsample:
L↑
M↓
In principle:
L↑
M↓
However:
Upsampling → introduce spectral copies at integer multiples of the original frequencies
Downsampling → risk of going below Shannon Nyquist [2] limit, thus introducing aliasing
[2]: https://en.wikipedia.org/wiki/Nyquist–Shannon_sampling_theorem
Notes: Aliases out of audible range may still be a problem, not for our ears but for audio devices (e.g., your tweeters might not like them) and processors.

## Slide 9
SRC Theory
Basic Implementation:
L↑
M↓
Replace
With
L↑
M↓
Low-pass filter
+ aliasing
no aliasing

## Slide 10
SRC Quality Metrics
Aliasing:
Presence of artifacts caused by the conversion

## Slide 11
SRC Quality Metrics
Aliasing:
Presence of artifacts caused by the conversion
Signal-to-noise ratio (SNR):
Measure of how much noise the SRC adds to the signal.

## Slide 12
SRC Quality Metrics
Aliasing:
Presence of artifacts caused by the conversion
Bandwidth:
% of the full bandwidth at which SRC operates
Signal-to-noise ratio (SNR):
Measure of how much noise the SRC adds to the signal.

## Slide 13
SRC Quality Metrics
Conversion speed:
Aliasing:
Presence of artifacts caused by the conversion
Inverse of conversion time
Bandwidth:
% of the full bandwidth at which SRC operates
Signal-to-noise ratio (SNR):
Measure of how much noise the SRC adds to the signal

## Slide 14
Simple SRC Showcase

## Slide 15
Simple SRC Performance
SNR | Bandwidth % | Speed
130 dB | 95,23% | SLOW

## Slide 16
Multirate SRC
Strategies for increasing SRC speed while maintaining good conversion quality
Idea[3]: filter at the lowest possible rate
[3]: https://authors.library.caltech.edu/records/rmhds-22q28
L↑
M↓
Low-pass filter
The system operates at the maximum sampling frequency
→ High computational cost
L↑
M↓
M↓
M↓
.
.
.
.
.
.
.
.
.
L↑
L↑
.
.
.
Decomposition
Polyphase filtering
Reconstruction

## Slide 17
Multistage SRC
SRC can be done in multiple conversion stages:
Operate on smaller signal portions (thus reducing complexity)
Use multiple filters (one per stage)
Each stage can be whatever SRC system
…
Overall sample rate conversion factor

## Slide 18
Multi SRC Showcase

## Slide 19
Comparison
SRC from 44.1 kHz to 48 kHz, comparison of different methods
[4]: https://docs.scipy.org/doc/scipy/reference/generated/scipy.signal.upfirdn.html
Method | SNR | BW % | Speed
Simple SRC | 130 dB | 95,23% | SLOW
upfirdn | 129 dB | 95,18% | FAST
Proposed Multirate Multistage | 125 dB | 95,23% | FAST
Simple SRC
SciPy upfirdn [4]
Proposed Multirate Multistage

## Slide 20
Thank You!
Check out our SRC demo online:
dspcraft.com/src
If you have any questions or comments reach out!
christian.gilli@dspcraft.com
michele.mirabella@dspcraft.com