## Slide 2: Golden Sun 1 & 2
Golden Sun 1
Released in August 2001 (JP), February 2002 (EU)
Golden Sun 2 The Lost Age
Released in June 2002 (JP), April 2003 (EU)
Developed by Camelot Software Planning
Music composed by Motoi Sakuraba

## Slide 3: About me
Audio programmer in the game industry for 12+ years
Worked for Quantic Dream, Rocksteady, Ubisoft, Compulsion Games… and now freelance.
Passionate about:
  old game soundtracks
  synthesizers

## Slide 4: What are we trying to do?
Mono
speaker
3.5mm stereo headphone jack
Game Boy Advance (2001)
Two audio sub-systems:
Sound generator inherited from the original Game Boy
(4 programmable channels: Square 1, Square 2, Wave, Noise)
Stereo sample playback with Digital-to-analog converter
(8-bit PCM, with sample rates varying between 5kHz and 42 kHz)
Game cartridge:
4 to 32 MB of data
Music composed on hardware synths and modules
Final output
(resampled to 32.768kHz, 9-bit)
Data
converted and
compressed
In-game mix

## Slide 5: What is game music restoration?
Analyze, research and reverse-engineer the console hardware and game data
Search for the original samples in high quality before they got compressed
Extract the original music sequences as MIDI files (when possible)
Recreate the tracks from scratch with the updated samples and sequences
Use modern mixing techniques

## Slide 6: Extracting the data
GBA Mus Ripper:
Tool created in the 2000s by Bregalad (not maintained anymore)
The GBA sound driver (MP2k/m4a/sappy) was reverse-engineered and documented
Locates the sequence structures and sample data
  Creates midi files and a soundfont containing the samples

## Slide 7
0xBC | Key shift - 0
0xC2 | LFO Speed
0cBB | Tempo - 0x41 x 2 = 130 BPM
0xBD | Set Instrument - 0x30 (48)
0xC8 | Master tune 0x40 (64 : no change)
0xC3 | LFO Delay: 0x3c
0xC4 | LFO Depth
0xC0 | Pitch Bend value: 0x40
0xBE | Set Volume to 0x45 (69)
0xBF | Set Panning to 0x40 (64: center)
0x8C | Delta time of 0x8C - 0x80 = 0x0C
0xF2 | NoteOn with auto NoteOff - Key: 0x40 (E4), Velocity: 0x40, 0xF2: duration
0xF2 | NoteOn with auto NoteOff - Key: 0x43 (G4), Velocity: 0x8C, 0xF2: duration

## Slide 8: Extracting the data
You can play the MIDI files using a soundfont VST in your favourite DAW.

## Slide 9: Where to find the original samples?
Video Game Music Sources community (collaborative database / Discord)
Roland SC-88 Pro
Cyanne on
Youtube

## Slide 10: Where to find the original samples?
Video Game Music Sources community (collaborative database / Discord)
Roland SC-88 Pro
Roland JV-1080
Expansion card
SR-JV80-05 World

## Slide 11: Where to find the original samples?
Video Game Music Sources community (collaborative database / Discord)
Personal research

## Slide 12: Restoring the samples
Example: Bass instrument
« Picked Bass » recorded from the Roland SC-88 (24-bit, 44100 Hz)
Extracted from the GBA cartridge (8-bit, 31 536 Hz)

## Slide 13: Restoring the samples
Example: Sitar Gliss
« Sitar Gliss » recorded from the JV-1080 + World expansion card (24-bit, 44100 Hz)
Extracted from the GBA cartridge (8-bit, 31 536 Hz)

## Slide 14: Restoring the samples
Edit the soundfont, replace the original samples with the restored ones
(adjust ADSR and panning if necessary)
Viena SoundFont Editor
Reaper

## Slide 15: Single sample vs Full patch

## Slide 16: Single sample vs Full patch
Example that doesn’t work: “Brass ff” in Venus Lighthouse:
Conclusion:
Some sounds will work great in their « full patch » version
Some sounds will work better if we stick to single patch
Recording 1: played on the SC-88 (full patch)
Recording 2: extracted and played with SF2 VST (single sample)
Example that works: “BrightStr” in The First Book
Recording: played on the SC-88 (full patch)

## Slide 17: Python scripts to improve the workflow
Identify the samples (and give them friendly names)

## Slide 18: Python scripts to improve the workflow
Identify the samples (and rename them)
Write scripts to get statistics so you can plan ahead

## Slide 19: Python scripts to improve the workflow

## Slide 20: Reaper script in Lua to improve the workflow
ReaScript to modify and route the midi files
Conversion rules in a json file

## Slide 21: Reaper script in Lua to improve the workflow

## Slide 22: Golden Sun’s custom synths
Custom synths hacked into the game by the Camelot devs
Three types
Multiple presets (different ADSRs)
Custom parameters
PWM
Sawtooth
Triangle

## Slide 23: Golden Sun’s custom synths
Approach 1: isolate and record synths from the rom
Approach 2: reverse engineer the synths
Thanks to Michael Panzlaff (ipatix) for reverse-engineering the synths!

## Slide 24: Agbplay by ipatix
agbplay
GBA rom
Direct output
or export to wav

## Slide 25: Turning agbplay into a VST
Direct output
Midi files
+ soundfont
+ wav samples
VST plugin
External dependencies:
Juce framework
TinySoundFont by schellingb

## Slide 26: Additional challenges
Alesis DM5
GS1 Drumkit
GS2 Drumkit
Mario Tennis
Drumkit
The search for drum sounds

## Slide 27: The search for drum sounds
Example: Ride Cymbal 1 (#51)
Extracted from Mario Golf Toadstool Tour, GameCube (16-bit, 32 kHz)
Extracted from Golden Sun 2, GBA (8-bit, 31 536 Hz)

## Slide 28: Other challenges
The search for drum sounds
Custom LFO (modulation): tempo-based pitch bending (BPM affects update rate)
Some samples were altered in post-production (ex: Steel Drums)

## Slide 29: Final mix

## Slide 30: Examples of restored tracks
Drums of Daila (Golden Sun 2, track 8)
Restored version
Original version (GBA)

## Slide 31: Examples of restored tracks
Boss Battle (Golden Sun 2, track 11)
Restored version
Original version (GBA)

## Slide 32: Thank you!
All my source code is available on:
https://github.com/justedni
Youtube channel with the full restored soundtrack:
https://www.youtube.com/@JusteDni
(or just google “Vincent Dortel”)
Special thanks
Coaltergeist, Cyanne
FreeJusticeHere, ipatix, TheAdorableOsha
Recommended Youtube channels
(about game music restoration)
Mathew Valente (tssf)
Jammin’ Sam Miller